## Slide 1: Pyrotex® KE
A single Solution for Hot-Gas Particulate and NOx Control

## Slide 2
Temperature 1,560F / 850°C
With or without NOx Catalyst
Calcium-Magnesium-Silicate fibers (CMS)
CMS fibers are bio degradable
Superior chemical resistance
Light-weight construction
High Air permeability of 5 – 35 [l/dm² min] @200 Pa
Conical Collar
T-shaped Collar

## Slide 3
Injection of:
SOx: Ca(OH)2 - (350oC)
Particulate Control
PM 2.5, PM 10
All in One Emission Control
Particulate, SOx, NOx,
< 1 mg/Nm3
NOx: NH3 - >95%

## Slide 4
Benefits Cement Plant, 3000 tclinker/day
Conversion to Pyrotex® KE
Potential savings:
1 Mega Joule/10tcinker

## Slide 5
Rotary Kiln
Cooling
Tower
Raw Mill
Raw Material
Preheater
Main Stack
ESP
Tires
Fuel
Pilot
Filter
Pilot Filter in a Cement Plant
Bypass Filter

## Slide 6: Catalyst Development
Chart: Temperature in °C
| 200 | 250 | 300 | 350 | 400 | 450 | 500
KEKAT-1 | 23 | 75 | 94 | 99 | 100 | 100 | 100
KEKAT-2 | 89 | 97 | 99 | 94 | 82 | 66
KEKAT-3 | 76 | 97 | 100 | 100 | 100 | 99
Zeolite and Vanadic Catalysts

## Slide 7
0.58 mm
Dust Layer
Dust Penetration

## Slide 8
Glass industry
Incineration - Biomass and Waste
Calcination - Aluminium
Gasification - Wood, Biomass, Residues
Pyrolysis – contaminated soil
Melting process
Carbide oven
Separation of precious metals
Reprocessing of radioactive materials
Cement industry
Pyrotex® KE Experience

## Slide 9
Cell Plate
Candle Element
Sealing Felt
Top Plate
Spacer Ring
Clamping System

## Slide 10
UV Test Results

## Slide 11
Cement Clinker Cooler
Filter with 2 compartments (1 compartment Pyrotex® KE)
T-shaped elements: 2.400 each
Temperature: toperation = 300°C tpeak = 400°C
A/C-Ratio: 0,65 nominal
Particulates: < 10 mg/Nm³
1 full cleaning cycle per day @ 2 bar; Δp = 10 mbar

## Slide 12
Pyrotex® KE
Cake Release

## Slide 13: Thank you very much